## Slide 1: Geothermal Project Management February – March 2024
Day 3 Session 3
Reservoir Engineering Concepts
Michael Gravatt and Team
Engineering Science & Geothermal Institute
University of Auckland, New Zealand

## Slide 2: Reservoir engineering tasks
Understand what is going on underground (permeability structure, temperatures and pressures)
Carry out and interpret various well tests
Suggest monitoring and testing programs
Help optimise and manage the reservoir performance

## Slide 3: Topics covered
Geothermal systems
Discussion of heat and mass underground
Darcy’s Law and implications
Downhole measurements
(Quite a lot of background theory to help understanding of geothermal reservoir behavior)

## Slide 4: Geothermal Modelling Group
Created by Professor Mike O’Sullivan
Led by Professor Mike O’Sullivan and Dr John O’Sullivan
The largest dedicated geothermal reservoir modelling team in the world
9 full-time geothermal reservoir modelling consultants
2 additional full-time specialists in modelling uncertainty
5-6 international interns annually
High quality geothermal modelling PhD candidates and Masters students also contribute

## Slide 5: Geothermal Modelling Group

## Slide 6: Geothermal Modelling Group
Modellers/consultants/researchers
Uncertainty quantification
Software developers
Group leaders

## Slide 7: Types of geothermal systems
At geothermal areas the heat flow is much larger than the world average of 60mW/m2
The type of geothermal system depends on the heat flow and the geological setting (discussed earlier)
They range from warm water systems where there is no fluid movement and no boiling up to convecting two-phase systems with lots of boiling underground

## Slide 8: Approximate thermodynamic classification of geothermal systems

## Slide 9: Approximate thermodynamic classification of geothermal systems

## Slide 10: Convective geothermal system

## Slide 11: Heat transfer mechanisms in geothermal systems
Conduction:
Heat flow = conductivity x temperature gradient
Convection:
Heat flow = mass flow x enthalpy
Counter-flow:
Heat flow = steam rising – water trickling down

## Slide 12: Heat transfer in geothermal systems

## Slide 13: Geothermal reservoirs
A geothermal reservoir is quite different from an oil or gas reservoir, or even a ground water reservoir.
First, a geothermal reservoir is usually not a clearly defined highly permeable region confined by low permeability strata;

## Slide 14: Geothermal reservoirs
Secondly the quantity to be extracted, namely heat energy, is not contained entirely in the reservoir fluid.
In an oil reservoir, once the oil has been extracted the reservoir is exhausted, but in a geothermal reservoir the water (or steam) which was originally in the reservoir can be replaced by surrounding cooler water which is heated by the reservoir rock and then becomes available for production.
This process of recharge is very important in the behaviour of geothermal reservoirs.

## Slide 15: Geothermal reservoirs
This process of recharge is very important in the behaviour of geothermal reservoirs.

## Slide 16: Reservoir engineering parameters
The most important reservoir parameters are porosity and permeability
Porosity measures how much pore space is available in the rock matrix
Permeability measures how well the pore space is connected (often related to the amount of fracturing)

## Slide 17
Porosity and permeability
Porosity and permeability can be primary (matrix) or secondary (fractures)
Rock grains
Rock grains
Primary porosity

## Slide 18: Reservoir engineering parameters - porosity
Porosity f is defined as the ratio of volume of pore space (i.e. the volume that can be occupied by the fluid) to the total volume of the system.
Porosities are of the order 5 -30% in the production zone of a geothermal reservoir.
However in the tighter surrounding rock porosity may be 1 % or lower.

## Slide 19: Reservoir engineering parameters -volume flux and fluid velocity v, u
The volume flux or Darcy velocity, v, is the flow rate per unit cross-sectional area of the porous medium.
The average velocity at which the fluid actually flows through the porous medium is known as the interstitial velocity, u. This is the particle velocity.

## Slide 20: Relationship between volume flux v and fluid velocity u
Here A is the cross-sectional area of the channel, v is the x-component of the volume flux v and Dx is the distance along the channel the injected fluid particles move during time Dt.
Rearranging the formula above gives an expression relating the volume flux to the particle velocity

## Slide 21: Relationship between volume flux v and fluid velocity u
Thus in general
Here v has units of velocity, namely distance/time. Typically the flux velocity is of the order 10-6 m/s.
In geothermal reservoir engineering usually mass flow Fm rather than volume flow v is used. For single-phase flow of hot water it is related to the volume flux by
Note that in calculating movement of chemicals, such as tracers or chlorides, the particle velocity u must be used

## Slide 22: Reservoir engineering parameters - permeability
We have to define a parameter which tells us how easy it is for fluid to flow through a porous medium (e.g. fractured rock).
This parameter is known as the permeability, k, and is defined by an empirical relationship known as Darcy's law, which can be expressed for one-dimensional flow of cold or warm water by (more details given later)

## Slide 23: Reservoir engineering parameters - permeability
The constant of proportionality is k/m, the permeability divided by the dynamic viscosity of the fluid.
For the same pressure gradient, a medium with a high permeability will allow a higher flux velocity than one with a lower permeability (k/m is sometimes called the mobility in petroleum engineering).
In terms of mass flux Darcy's law becomes
Kinematic viscosity

## Slide 24: Reservoir engineering parameters - permeability
Permeability may be directional; that is, larger in one direction. A system such as this is said to be anisotropic.
One in which the permeability is the same in all directions is said to be isotropic. Geothermal systems frequently have anisotropic permeability.
The units of permeability are those of area, i.e., m2.

## Slide 25: Reservoir engineering parameters - permeability
Typical values of permeability in a geothermal system are of the order 10-14 m2, with vertical permeability perhaps 4-5 times smaller.
One special unit often used is the darcy which is approximately equal to 10-12m2
Or the millidarcy which is approximately equal to 10-15m2. Typical values of permeability for geothermal systems are shown below

## Slide 26: Reservoir engineering parameters - permeability

## Slide 27: Porosity and permeability
Porosity and permeability can be primary (matrix) or secondary (fractures)
Low 2nd porosity, Low 2nd perm
High 2nd porosity, Low 2nd perm.
High 2nd porosity, High 2nd perm.
Rock grains
Rock grains
Primary porosity

## Slide 28: Other reservoir engineering parameters

## Slide 29: Heat and mass underground
Mass. The amount of water and steam underground, per unit volume of the reservoir, is given by
Here f is the porosity, rl and rv are the densities of the liquid and vapour (or gas) phases, respectively, and Sl, Sv are liquid and vapour saturations, respectively.
Amount of vapour
Amount of liquid

## Slide 30: Saturations
The saturations Sl, Sv are the volume fractions of liquid and vapour.
They are commonly used in reservoir engineering to measure the proportions of water and steam
Whereas for surface equipment engineering, "dryness" is usually used.
Note:

## Slide 31: Heat and mass underground
Similarly the energy content is given by
Here rr, cr are the rock density and rock specific heat respectively and ul, uv are the specific internal energies for liquid and vapour.
Energy in the rock is much more significant, but heat is transported in the fluid
Energy in the rock
Energy of the fluid

## Slide 32: Stored heat calculations
A simple method for calculating the production potential of a geothermal reservoir is to carry out a stored heat calculation.
Volume:
@ 240 °C

## Slide 33: Stored heat calculations
A simple method for calculating the production potential of a geothermal reservoir is to carry out a stored heat calculation.
Thermal energy (kJ)
Reservoir area (m2)
Reservoir thickness (m)
Reservoir Temperature (°C)
Rock specific heat (kJ/kg/K)
Rock density (m3)
Ambient Temperature (°C)

## Slide 34: Stored heat calculations
Energy in the system

## Slide 35: Stored heat calculations

## Slide 36: Stored heat calculations
Electrical power output is obtained by combining the recovery factor (), efficiency () and parasitic losses.
Which for our example gives 188 MW with = 15.5%, = 10% and Pparasitic = 4 MW.
But what if we don’t know all these values?
Pe = h r PThermal – PParasitic

## Slide 37: Stored heat calculations
The problem is that the magnitude of the recovery factor is unknown.
Values in the range 0.1 - 0.5 have been suggested by various authors but no really convincing reasons have been given for the choice.
Some workers have suggested that the calculation of the final energy should not be based on a final state of the reservoir containing cold water, because the reservoir will cease useful production when the final temperature is at some higher value, say ~180oC for electricity production.

## Slide 38
Example: Stored heat calculation
Inputs
Outputs
38

## Slide 39
Example: Stored heat calculation
Inputs
Outputs
39
What happens if the average reservoir temperature is lower?

## Slide 40
Example: Stored heat calculation
Inputs
Outputs
40
What happens if we were more certain about the reservoir parameters?

## Slide 41: Flow in geothermal reservoirs - Darcy’s Law
In 1856, Henry Darcy, a French hydraulic engineer, reported that he had found that the flow rate in a porous medium is proportional to pressure difference and inversely proportional to the length of the flow path.
Thus

## Slide 42: Darcy’s Law Experiment
Q
p2
p1
l

## Slide 43: Darcy’s Law
Darcy introduced the permeability k
Volume
Mass

## Slide 44: 3D version of Darcy’s Law
X-direction
Y-direction
Z-direction
(z is measured vertically upwards in my notation)
Effect of gravity

## Slide 45: 3D permeability
Johri et al. 2014
ky
kx
kz
kx < kz < ky
Anisotropic Permeability

## Slide 46: Anisotropic, 3D version of Darcy’s Law
X-direction
Y-direction
Z-direction
Permeability and hence flow can be different in each direction e.g. along faults, between different formations etc.

## Slide 47: Groundwater notation
In groundwater studies, reservoir engineers usually use head rather than pressure
Pressure measured in terms of depth of water
Elevation
Total head

## Slide 48: Groundwater notation- 3D Darcy’s Law
The gradient in head is what drives the flow. Water flows down hill and from high to low pressure.
Because of the temperature differences and therefore density differences head is not a useful quantity to use in geothermal reservoir engineering. We use pressure instead.

## Slide 49: Groundwater vs Geothermal
Geothermal flows are non-isothermal
Boiling can occur
Vertical flows are more important in geothermal fields
Coupling of heat and mass flows

## Slide 50: Two-phase version of Darcy’s Law
The basic idea is that the two phases, water and steam, interfere with one another
The same kind of process occurs in an oil reservoir where gas and liquid oil may both be present
A separate Darcy’s Law equation is written for each phase

## Slide 51: Two-phase version of Darcy’s Law
Water
Steam
Total
Relative permeability between 0 and 1

## Slide 52: Relative permeabilities
The relative permeabilities or permeability reduction factors krl, krv account for the fact that the liquid and vapour phases interfere with one another as they move through the fractured rock matrix.
The exact forms of krl and krv are not really known but it is known that they depend on the liquid saturation

## Slide 53: Relative permeabilities
This interference between the phases is one of the most important aspects of two- phase flow in a porous material.
At high liquid saturations the liquid (water) flows while the vapour (steam) remains immobile.
At low saturations the liquid becomes immobile and the vapour moves.

## Slide 54: Relative permeability curves
Corey curves for Slr = 0.30, Svr = 0.05

## Slide 55: More relative permeability curves
Chart: Liquid saturations
Linear curves for Slr = 0.30, Svr = 0.05

## Slide 56: Energy flow
Darcy's Law also affects the calculation of the energy flux.
For single phase flow of hot water the energy flux is given by
Here hl is the enthalpy and K is the thermal conductivity
Convection
Conduction

## Slide 57: Energy flow
For a two-phase flow of water and steam it is given by
Convection
Conduction

## Slide 58: Energy and enthalpy
For a static sample use internal energy, but for a moving fluid use enthalpy
internal energy
enthalpy

## Slide 59: Simple flows
We will now look at simple flows and the implications of Darcy’s Law
First we will consider 1D radial flow towards a geothermal well

## Slide 60: Flow towards a well
feed zone
Horizontal, radially symmetric flow

## Slide 61: Plot of effective kinematic viscosity (using Corey’s curves)
Viscosity depends on the proportion of vapour and liquid, highest when both are present. This affects the fluid flow underground.

## Slide 62: Two-phase flowing enthalpy (using Corey’s curves)
Choice of relative permeability curves affects the flow enthalpy predicted.

## Slide 63: Temperature profiles
A
B
C
D

## Slide 64: 1D vertical flow in upflow zones

## Slide 65: Warm water systems

## Slide 66: Hot Water Systems
For most of the upflow zone the temperature gradient is very small; hl remains approximately constant as the pressure p changes, while the temperature T remains approximately constant.
Near the surface the temperature decreases rapidly and the conductive transfer increases to match the decrease in hl.

## Slide 67: Hot water upflow zone
conduction
convection

## Slide 68: Two-phase upflow zone
Where a boiling zone occurs the temperatures and pressures are close to the boiling-point-with-depth curve.
A small amount of energy is transported by conduction but most is moved by counter-flow of water falling and steam rising.
Above the two-phase zone a liquid condensate layer occurs, with large temperature gradients transporting most of the heat.

## Slide 69: Two-phase upflow zone
Pressures follow a slightly greater than hydrostatic gradient.
At depth (deep brine) the liquid zone requires large temperature gradients to produce a large energy flux accompanied by a small mass flux.

## Slide 70: Two-phase upflow zone

## Slide 71: Saturation in upflow zone

## Slide 72: Profiles for a vapour dominated system

## Slide 73: Well-test analysis

## Slide 74: Completion test
Often done soon after drilling is finished
Inject cold water (often change rate during test – step rate up or down)
Carry out pressure-temperature-spinner (PTS) run
Deduce location of feedzones from changes in spinner signal and changes in temperature
Allow well to warm up. Carry out repeat PT runs
Deduce reservoir temperature profile from 2-3 week warm-up curves

## Slide 75: Spinner data
From Hole, 2008

## Slide 76: Temperature data
From Hole, 2008

## Slide 77: Warm-up curves
From Hole, 2008

## Slide 78: Downhole temperature profiles
After the completion test and a warm-up period (2-3 weeks) stable down-hole temperatures can be measured
Downhole temperature profiles may require interpretation as well temperatures and reservoir temperatures may not be the same (e.g. internal flows, wells on bleed)

## Slide 79: Down-hole temperature profiles
Could be down-flow

## Slide 80: Down-hole temperature profiles
Steam upflow

## Slide 81: Down-hole temperature profiles
Boiling point for depth curve

## Slide 82: Transient well tests
Used by reservoir engineers to diagnose reservoir performance
Control flow rate in a well
Measure downhole pressure in the same well or a nearby well
From a plot of pressure vs time (semi-log or log-log) calculate kh (permeability-thickness product) and fCh (porosity-compressibility-thickness)
Sometimes estimate other parameters (skin, wellbore storage, boundary effects)

## Slide 83: Transient well tests
Common tests
Drawdown/buildup
Injection/falloff
Interference
In geothermal, buildup, falloff and interference tests are the most common
Usual methods of analysis may not work because of boiling and condensation – use a simulator instead

## Slide 84: Well test analysis (continued)
The most important parameter is D the diffusivity
It measures how fast pressure changes spread around a reservoir. For a hot water reservoir both the water and rock compressibility are very small. Thus pressure changes spread a long way, very fast
Flow parameters
storage parameters

## Slide 85: Well test analysis (continued)

## Slide 86: Output tests
Measure flow rate, well-head pressure and often enthalpy
Useful for showing change in reservoir conditions
From Grant, Donaldson & Bixley

## Slide 87: Tracer tests
Tracer tests provide information on the nature and properties of connections, or flow-paths, between reinjection and production wells
These connections control the rate of cooling of the production wells during long-term reinjection of colder fluid
Thus tracer tests help to identify the possibility of “thermal break-through”
Thermal breakthrough time (onset of cooling) is usually several orders of magnitude (2–4) greater than the tracer breakthrough time

## Slide 88: Liquid-phase tracers:
Halides such as iodide (I) or bromide (Br);
Radioactive tracers such as the isotopes iodide-125 (125I) and iodide-131 (131I);
Fluorescent dyes such as fluorescein and rhodamine;
Aromatic acids such as benzoic acid;
Naphthalene sulfonates.

## Slide 89: Steam and two-phase tracers
Steam-phase tracers:
Fluorinated hydrocarbons such as R-134a and R-23;
Sulphur hexafluoride (SF6).
Two-phase tracers:
Tritium (3H);
Alcohols such as methanol, ethanol and n-propanol.

## Slide 90: Tracer test results
Axelsson, 2013

## Slide 91: Tracer test result
Axelsson, 2013

## Slide 92: Monitoring data (well–by-well)
Mass flow
Production enthalpy
Downhole pressure
Chemistry (gas and/or chloride etc)

## Slide 93: Things that go wrong
Pressures drop too low
Enthalpies decline (shallow wells and wells near the edge of the field)
Injection returns and thermal breakthrough
Chemical problems –calcite or silica deposition

## Slide 94: Thank you!