## Slide 1
Day 3 Session 4
Geothermal Reservoir Modelling
Michael Gravatt and Team
Engineering Science & Geothermal Institute
University of Auckland, New Zealand
Geothermal Project Management February – March 2024

## Slide 2: Outline
Introduction to modelling
Geothermal modelling process
Modelling uses
Limitations

## Slide 3: Introduction to modelling
Modelling is used everywhere
Formula 1
Populations
Climate
Physiology

## Slide 4: Why make models?
To help understand what is happening or has happened
Sometimes we can’t measure what happened:
  Things are too small or happen to fast
  You can’t reach what you want to measure – eg deep underground
  Measuring data can affect the results – eg pressure sensors on planes
  You can’t always put things inside people!

## Slide 5: Why make models?
To make predictions about what will happen in the future
  Important for planning – eg budgets
  Can save a lot of money – eg design costs
  Can save a lot of time
  Build confidence in decisions – not just from model results but also modelling process

## Slide 6: What do models look like?
  Simple formula with a few parameters
  Spreadsheet
  Large complex models based on breaking up the 3D region of interest into many small pieces (finite volume or finite element methods), implemented with simulation software
  Model parameters must be selected so that the model results match past history (calibration process)

## Slide 7: A simple example – matching population growth

## Slide 8: A simple example
1st attempt:
Period | 
Pre-Agriculture | 0.0003
Pre-Industrial | 0.0003
Post- Industrial | 0.0003
Modern | 0.0003

## Slide 9: A simple example
2nd attempt:
Period | 
Pre-Agriculture | 0.0003
Pre-Industrial | 0.0005
Post- Industrial | 0.0005
Modern | 0.0005

## Slide 10: A simple example
3rd attempt:
Period | 
Pre-Agriculture | 0.0003
Pre-Industrial | 0.0007
Post- Industrial | 0.0007
Modern | 0.0007

## Slide 11: A simple example
4th attempt:
Period | 
Pre-Agriculture | 0.0003
Pre-Industrial | 0.0007
Post- Industrial | 0.005
Modern | 0.005

## Slide 12: A simple example
5th attempt:
Period | 
Pre-Agriculture | 0.0003
Pre-Industrial | 0.0007
Post- Industrial | 0.005
Modern | 0.0175
This process is called model calibration

## Slide 13: A simple example
Our calibrated model matches historic data
Now we can use it predict the future

## Slide 14: Geothermal models
Geothermal models are like our example
They are based on laws and calibrated using real data
There a many different types of geothermal models ranging in complexity – simple lumped parameter up to complex 3D models with 100,000 to 1,000,000 blocks
Stored heat calculations are very simple “models” that follow the Conservation of Heat Law:
Useable Heat = Total Heat – Unusable Heat
(energy you take out) (energy in the ground) (energy that stays in the ground)

## Slide 15: Geothermal models
Geothermal reservoir models are much more complicated and follow several laws:
Conservation of Mass
  “What goes in must come out”
Conservation of Heat
  “Energy cannot be created or destroyed”
Darcy’s Law
  Define how hot water and steam move underground

## Slide 16: Geothermal models
Before talking about model uses and limitations it is helpful to understand how geothermal models are made

## Slide 17: Geothermal modelling initial process
Gather and analyse data
Create a conceptual model of the geothermal system
Build an calibrate natural state model consistent with the conceptual model
Use the natural state model to make a production model and calibrate with production history data
Run future scenarios using the production model
Steps 3 to 5 are iterative
Leapfrog
Leapfrog
Leapfrog

## Slide 18: Geothermal modelling update process
Update data and analysis
Update the conceptual model
Update the natural state model ensuring it is consistent with the updated conceptual model
Use the natural state model to make a production model and calibrate with production history data
Run future scenarios using the production model
Steps 3 to 5 are iterative
Leapfrog
Leapfrog
Leapfrog

## Slide 19: Gather and analyse data
Gather as much data as possible
From a wide variety of sources:
  Geosciences
  Environmental sciences
  Engineering
  Hydrological
Data collected before production occurs is very important!
Some things are impossible to understand before wells are drilled

## Slide 20: Conceptual model
Combines and distils all the available data
Provides a “conceptual” idea about how the geothermal system behaves
Details are discussed in a separate lecture

## Slide 21: Conceptual model to numerical Model
New tools to create Geological/Geophysical models integrated with numerical reservoir models using LEAPFROG® and TOUGH2
Ensures consistent system representation and allows early numerical model development

## Slide 22: Model design
Size and shape of model
Number of blocks, block refinement
Boundary conditions on top, sides and base
Geological structure
All very important matters, but will not be discussed today (we need many more lectures on modelling)

## Slide 23: Natural state model
A reservoir model of the system before any production occurred
Model calibrated using pre-production data:
  Exploration well data
  Surface features (geysers, hot pools, springs etc)
  Completion test data from the first production wells
  Downhole temperatures (after heating up!)

## Slide 24: Production model
Reservoir model follows the production history for the system
Transient data are used to calibrate the model
  Pressure decline
  Enthalpy changes
  etc

## Slide 25: Future scenarios
Once a model has been calibrated using natural state and production data it can be used to predict the future
The more good data used for calibration the more accurate the predictions are likely to be
Scenarios are set up that define expected future production, well locations, reinjection strategies etc
How scenarios are created depends on what the model is to be used for

## Slide 26: Modelling uses
Geothermal reservoir models are mainly used to predict the following:
  How long a system can be economically exploited
  What new wells are required to maintain production
  How a system will respond to different rates of production
  How to best re-inject fluid into a system
  How the natural geothermal features will react to the systems exploitations
  What other environmental effects may occur
  What is the resource potential of a system?

## Slide 27: Modelling uses
Which of these are important to a developer?
  How long a system can be economically exploited
  What schedule of new wells are required to maintain production
  How a system will respond to different rates of production
  How to best re-inject fluid into a system
  How the natural geothermal features will react to the systems exploitations
  What other environmental effects may occur
  What is the resource potential of a system?

## Slide 28: Modelling uses
Which of these are important to a policy maker?
  How long a system can be economically exploited
  What schedule of new wells are required to maintain production
  How a system will respond to different rates of production
  How to best re-inject fluid into a system
  How the natural geothermal features will react to the systems exploitations
  What other environmental effects may occur
  What is the resource potential of a system?

## Slide 29: Modelling uses
Reservoir models are also used for scientific research
  How do geothermal systems form and why?
  How do geothermal system interact?
  What are the fundamental processes that occur in geothermal systems?
  etc

## Slide 30: How long a system can be economically exploited
In most cases the amount of energy taken out of a geothermal system by production is more than the natural recharge
Natural recharge
Energy taken out

## Slide 31: How long a system can be economically exploited
At some point it will become uneconomic to continue exploitation and the production will have to stop while the pressure recovers in the system
This may be in 25 years, 35, 50 or even 100
Stored heat calculations give simple estimates, useful only as a first guess
Reservoir models represent the detailed physical processes and therefore are much more accurate

## Slide 32: How long a system can be economically exploited
Brief History of Wairakei:
  Started operation in late 1958
  Pressures dropped quite soon
  Pressure decline of 25bar by 1965
  Panic! Send for the modellers!
  It has settled down and continues on, perhaps for 100 years

## Slide 33: How long a system can be economically exploited
In New Zealand regulators require reservoir models to be used as part of the permitting process
In many other countries it may become a requirement for companies listed on the stock exchange

## Slide 34: What schedule of new wells are required to maintain production
As pressure declines locally, wells will produce less.
Reservoir models are used to predict when new make-up wells must be brought online to maintain power production

## Slide 35: What schedule of new wells are required to maintain production
Reservoir models can also be used to plan extra capacity needed for regular maintenance

## Slide 36: How a system will respond to different rates of production
The rate of production affects how quickly pressure in a system declines
It also affects the schedule of new wells to be drilled
Different pressure decline
rates will affect the
environment differently
Tauhara expansion (source: Contact)

## Slide 37: How a system will respond to different rates of production

## Slide 38: How a system will respond to different rates of production

## Slide 39: How a system will respond to different rates of production

## Slide 40: How to best re-inject fluid into a system
Re-injection is carried out for two main reasons:
To slow down the rate at which the pressure in the system declines (pressure support)
To safely dispose of extracted fluid

## Slide 41: How to best re-inject fluid into a system
For pressure support reservoir
models are used for the
following:
  Indicate where best to re-inject
  How much to re-inject
  At what temperature
The objective is to support
production while avoiding
thermal breakthrough
(source: Kipyego 2013)

## Slide 42: How to best re-inject fluid into a system
For fluid disposal the objective is to determine where large quantities of fluid can be injected without affecting production or the environment
Can simulate tracer tests to improve calibration
Tracer simulations (source: Bjarkason 2014)

## Slide 43: How the natural geothermal features will react to the systems exploitation
Depending on the connection between them, surface features can be affected by production
In Rotorua in New Zealand a borehole closure programme was implemented in 1980 to protect important natural features

## Slide 44: How the natural geothermal features will react to the systems exploitation
(source: Ratouis 2014)

## Slide 45: How the natural geothermal features will react to the systems exploitation
There is renewed interest in more exploitation of the Rotorua system
Our reservoir model will be used to assess the likely impact of any future increase on protected surface features
(source: Ratouis 2014)

## Slide 46: How the natural geothermal features will react to the systems exploitation
In some cases production creates new surface features!
Models can help predict this
1953
1973
1993

## Slide 47: What other environmental effects may occur
Many environmental effects are controlled by the pressure and temperature in the geothermal system
Reservoir models predict these and so can be used to predict environmental effects
A common environmental effect is subsidence
Ohaaki Marae

## Slide 48: What other environmental effects may occur
Subsidence of nearly 10m affecting cultural meeting house
1978
Today

## Slide 49: What other environmental effects may occur
Ohaaki reservoir model
Subsidence rate per year (source: Allis)

## Slide 50: What other environmental effects may occur
Subsidence can also have an impact on the power plant
Expanding gap filled twice already

## Slide 51: Modelling uses
Small models of individual wells
Analyse well performance
Estimate well properties
Production or injection

## Slide 52: Limitations of Modelling
Do you think our estimate of global population will be correct?
No!
“All models are wrong…”
“… but good models are useful”
Every model has assumptions that limit what it should be used for and what it can tell us.
It is important to understand what reservoir models cannot tell us

## Slide 53: Drilling Success
Reservoir models cannot:
  Predict probability of drilling success
  Tell you exactly where to drill a well
  Predict exactly where good permeability exist
  Predict problems with casing, cementing etc
  Predict well performance before drilling
Reservoir models calibrated with good data can:
  Tell you where hot, high enthalpy fluid is most likely to be
  Predict where good average permeability exist
  Predict future well performance following initial testing

## Slide 54: Operations
Reservoir models cannot:
  Predict operational problems
  Predict mechanical failures
  Predict human error
  Predict economic decisions
Reservoir models can help:
  Plan contingency in resource availability
  Predict the effects of unexpected, long-term changes in production

## Slide 55: Chemistry
Standard reservoir models cannot:
  Predict where scaling will occur and how quickly
  Predict which wells will be affected by high NCG content
If you want predictions like these you must:
  Gather accurate data about chemistry in the system
  Include chemistry in the reservoir model – this can make models much more complicated
  Calibrate the model using the chemistry data
  For scaling the results from the reservoir model must often be used in another smaller model of the components in question

## Slide 56: Chemistry
Measured and modelled chloride concentrations (sources: Stewart, Setiadi)

## Slide 57: Calibration Data
It is very important for all aspects of a geothermal development that good data is gathered regularly
Models without much data for calibration or poor quality data are of limited use
Natural state data is important – if you don’t know where you started its hard to know where you will arrive!

## Slide 58: Statistics and uncertainty
Standard reservoir models are not statistical models
They can be used as part of Monte Carlo simulations but this can be computationally expensive
With fast new simulators and cloud computing it is now possible
Decision makers should now expect some analysis of uncertainty in their model forecasts

## Slide 59: Uncertainty Quantification
Use advanced modelling to run thousands of models to provide ranges of forecasts
Shows the uncertainty of model forecasts supporting much more robust decisions
This is called Uncertainty Quantification
Successfully applied to commercial projects:
  Ohaaki
  Lihir
  Rotorua
  Karaha
  Sungai Penuh
  Bukit Daun
  Sorik Merapi
Now a standard deliverable at GI

## Slide 60: Geothermal Resource Assessment
The traditional method for Geothermal Resource Assessment is a Stored Heat Calculation
Developed over 50 years ago
Very simple model to calculate the energy that can be extracted
Monte Carlo sampling is carried out over a very small number of parameters to create a range of forecasts
The Recovery Factor is a very important and very uncertain parameter in a stored heat calculation

## Slide 61: Geothermal Resource Assessment
Fast, Consistent Model Setup
Fast Simulations
with Waiwera
Mathematical Tools
Data Space Inversion
PEST
iTOUGH2
…
Uncertainty Quantification
Geoscience Exploration Data
Geothermal Resource Assessment

## Slide 62: Geothermal Resource Assessment
We use the best available geoscientific estimate of the system
Then we generate thousands of possible models
3D geological model in Leapfrog Geothermal®
Downhole Temperatures for Future Wells from thousands of possible models

## Slide 63: Geothermal Resource Assessment
We use the best available geoscientific estimate of the system
Then we generate thousands of possible models
But only keep the models that agree with the geoscience exploration data
3D geological model in Leapfrog Geothermal®
Downhole Temperatures for Future Wells from thousands of possible models

## Slide 64: Geothermal Resource Assessment
Then we run realistic maximum energy extraction scenarios on all remaining models using coupled wellbore simulations
Statistics for the resource potential can then be calculated:
P50 = 88MW
P90 = 37 MW
P10 = 150 MW

## Slide 65: Geothermal Resource Assessment
Stored Heat Calculation | Reservoir Modelling + Uncertainty Quantification
Uses a single, simple representation of the geology | Uses many different likely representations of the geology
Uses the resistivity boundary | Uses the full 3D resistivity data
No physics included in model or Monte Carlo samples | Subsurface physics included. Model samples that are not geothermal systems consistent with data are excluded
Only simple temperature data included | All measured exploration data can be included and used to constrain uncertainty
Relies on the problematic Recovery Factor | Realistic maximum production rates can be calculated for each sample including representative wellbore models

## Slide 66: Summary
Reservoir modelling is an invaluable tool for understanding geothermal systems and predicting their behaviour
It is important to know what questions the modelling is trying to help answer and what the model’s limitations are
Ensure the reservoir model is consistent with conceptual model of the system based on all the available data

## Slide 67: Summary
Make sure reservoir modelling work is done following best practices
Policymakers/regulators may start requiring this soon
Be cautious of modelling work that always gives you the results you hope for!
More in:
O'Sullivan, M. J., & O'Sullivan, J. P. (2016). Reservoir Modeling and Simulation for Geothermal Resource Characterization and Evaluation. In R. DiPippo (Ed.), Geothermal power generation: developments and innovation. Woodhead Publishing.

## Slide 68: Summary
Start modelling early!
Gather good data at the start of a project and continue throughout the project
Regularly update your model to ensure you get the most value out of it
Regard modelling as a routine, continuing process
Compared to the other costs in geothermal projects modelling is cheap!

## Slide 69
Thank you!